## Slide 1: P&S Modern SSDs Cutting-Edge Research in SSDs
Dr. Jisung Park
Prof. Onur Mutlu
ETH Zürich
Fall 2022
04 January 2023

## Slide 2: Outline
NAND Flash Basics
Reducing Solid-State Drive Read Latency by Optimizing Read-Retry, ASPLOS 2021
Evanesco: Architectural Support for Efficient Data Sanitization in Modern Flash-Based Storage Systems, ASPLOS 2020
DeepSketch: A New Machine Learning-Based Reference Search Technique for Post-Deduplication Delta Compression, FAST 2022

## Slide 3: NAND Flash-Based SSDs
A complicated embedded system
  Multiple cores, HW controllers, DRAM, and NAND flash chips
NAND Flash Chips
Persistent data store
LPDDR DRAM
Metadata store
SSD Controller
ARM Cores Running firmware
HW Flash Controllers Chip control, ECC
Samsung PM853T 960GB Enterprise SSD (from https://www.tweaktown.com/reviews/6695/samsung-pm853t-960gb-enterprise-ssd-review/index.html)
Unique characteristics
Erase-before-write
Limited endurance
High error rates
…

## Slide 4: Flash Cell
Stores data using its threshold voltage (VTH) level
  Dictated by the amount of electrons (i.e., charge) in the cell
  The more the electrons, the higher the VTH level
Flash Cell
Program:
Injects electrons
Erase:
Ejects electrons
Read:
Compares w/
reference level
1
0
1. Can change VTH (=charge) in a non-volatile manner
2. Encodes bit data with different VTH ranges

## Slide 5: Flash Cell Characteristics
Multi-leveling: A single flash cell can store multiple bits
Retention loss: A cell leaks electrons over time
Limited lifetime: A cell wears out after P/E cycling
11
01
00
10
2-Bit Multi-Level Cell (MLC)
1 year
1 year
11
01
00
10
11
01
00
10
11
01
00
10
00
Retention error!
1 year
@ 1K P/E cycles
1 year
@ 10K P/E cycles
11
01
00
10
11
01
00
10
00
Retention error!
11
01
00
10
1
0
Single-Level Cell (SLC)

## Slide 6: Page and Block
A number of flash cells operate in parallel
⋯
⋯
⋯
⋯
⋯
⋯
WL0
Cells in the same wordline (WL) are concurrently read/programmed
<100,000 cells
⋯
WL1
WL2
WL125
WL126
WL127
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Block (128 WLs)
Cells in the same block are concurrently erased
Long latency,
but high bandwidth
No overwrite of WLs
before erasing the block:
Erase-before-write
1
0
0
1
0
1
1
0

## Slide 7: Page and Block
A number of flash cells operate in parallel
⋯
⋯
⋯
⋯
⋯
⋯
WL0
Cells in the same wordline (WL) are concurrently read/programmed
⋯
WL1
WL2
WL125
WL126
WL127
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Block (128 WLs)
Cells in the same block are concurrently erased
⋯
Page (16 KiB)
Block (127 pages)
127
126
⋯
1
0
(16,384× 8 + α) cells

## Slide 8: Page and Block
A number of flash cells operate in parallel
⋯
⋯
⋯
⋯
⋯
⋯
WL0
Cells in the same wordline (WL) are concurrently read/programmed
⋯
WL1
WL2
WL125
WL126
WL127
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Block (128 WLs)
Cells in the same block are concurrently erased
Page (16 KiB)
Triple-Level Cell (TLC)
Block (127×3 pages)
4
3
2
1
0
⋯
381
380
379
378
⋯
Share the same cells (WL)
(16,384× 8 + α) cells

## Slide 9: P&S Modern SSDs Cutting-Edge Research in SSDs
Dr. Jisung Park
Prof. Onur Mutlu
ETH Zürich
Fall 2022
04 January 2023